## Slide 1: Electric Water Heater
Islam osama
Fady nagy
Mohamed hammad
Ziad abdel-rahem

## Slide 2: Introduction
The Electric Water Heater system:
is a project that combines both practical engineering and innovative programming.
Throughout this presentation, you will walk through the key components of the project, including the design, programming, and implementation processes. Moreover discussing the challenges faced, the solutions developed, and the results achieved.

## Slide 3
START
OFF STATE
ON/OFF PRESSED
INPUT DESIRED TEMPERATURE
NO
ON STATE
YES
UP/DOWN PRESSED
YES
NO
SETTING STATE
OUTPUT CURRENT / AVERAGE TEMPERATURE
OUTPUT
DESIRED
TEMPERATURE
UP/DOWN PRESSED
YES
NO
CURRENT TEMP >|< DESIRED TEMP
NO
YES
HEATER ON
COOLER ON
OUTPUT CURRENT / AVERAGE TEMPERATURE
FLOW CHART
LED ON
LED BLINK
ON/OFF PRESSED
CHECK
CHECK

## Slide 4: INTERFACES
There were multiple drives and devices that interfaced in conducting our project such as:
DRIVES:
ADC (Analogue to Digital Converter)
DIO (Digital Input Output)
EXTERNAL/GLOBAL INTERUPT
TIMER 0/TIMER 2
UART
INTERNAL EEPROM
ELECRONIC DEVICES:
MICROCONTROLER (ATMEGA 32)
HEATING ELEMENT
COOLING ELEMENT (PELTIER)
HEAT SENSOR (LM35)
ONE LED LIGHTS
THREE BUTTONS
SEVEN SEGMENT
INTERNAL EEPROM

## Slide 5: ADC (Analogue to Digital Converter)
The ADC converts the analogue signal value from the temperature sensor into a digital value (0-1), and it depends on two parameters.
The first parameter is the resolution and in our case ATMEGA32 the ADC resolution is 10-bit.
While, the second parameter is the maximum voltage and in our case it is 5 Volts.
ADC is used to take readings from the temperature sensor.
So, in the C-code “Tc = ADC_read(ADC_CH0)” , it takes the readings from the temperature sensor as an analogue signal and convert it to digital signal.

## Slide 6: DIO (Digital Input Output)
DIO is a driver to deal with digital signals, either by sending (Output) or receiving (Input) these signals.
So, this driver is used to initialize each pin whether it is output or input, to check each pin value when initialized as input and to set each pin value when initialized as output.
For ATMEGA32, we have 32-bit, divided as 4 registers (A,B,C and D) and each register consists of 8 bits (0 --> 7).

## Slide 7: EXTERNAL/GLOBAL INTERRUPTS
Interrupts are something happens to get us out of the super loop to do a specific mission and then return back to the super loop.
For any interrupt to occur, there are three things to take into consideration: a- PIE (Peripheral interrupt enable). B- PIF (Peripheral interrupt function). C- GIE (Global interrupt enable).
External interrupt is used for ON/OFF Button.

## Slide 8: TIMER0 / TIMER2
Timers is used to get a specific time by knowing the clock cycle and its period.
Timer used in the project is CTC (Clear timer on compare match), so we needed to know the following:
  Timer Resolution  8-bit.
  CPU frequency  16 MHZ.
  Prescaler Value  256.
  Timer frequency  CPU frequency/prescaler value = 16MHZ/256 = 62,500 HZ
  Tick Time  1/Timer frequency = 1/62,500 = 0.000016 sec
  Set OCR  249 is used.
So, in this project we needed two values 1 sec for LED and Seven segment blinking, and 100 msec for temperature sensor readings.
Applying the previous equations, to get 1 sec: Counter = desired time/ (OCR+1)* tick time = 1 sec / (249+1)*0.000016 sec = 250.
And, to get 100 msec: Counter = 100 msec / (249+1)*0.016 msec = 25.

## Slide 9: UART (Universal Asynchronous Receiver Transmitter)
UART is used to send and receive data between two different Microcontrollers.
Bluetooth is implemented in the project to be easily connected to any mobile phone.
UART is used in this project to give the user an easier way than buttons to control the equipment.

## Slide 10: INTERNAL EEPROM (Electrical Erasable Programable Read Only Memory)
EEPROM is a memory to save any non-volatile variable.
Internal EEPROM is used which is 8-bit of each byte.
It is used to save the last desired temperature when the power is off.

## Slide 11: PROBLEMS
We had a problem with synchronizing between all the functions of the code and we solved it by making every function separate and by using global variables and arrays.
Developing a user-friendly interface for controlling the water heater was more complex than anticipated. We faced challenges in designing an intuitive and responsive interface that allowed users to easily set and monitor water temperatures.
Integrating the hardware components (such as sensors, and the microcontroller) with the software posed several difficulties. Compatibility issues between different components required troubleshooting and adjustments in both the hardware setup and code.
The code had issues with timing and synchronization, particularly when coordinating between multiple tasks or modules. This affected the overall performance and timing accuracy of the heater. Refining the timing mechanisms and synchronization processes helped address these issues.

## Slide 12: Conclusion
The electric water heater project, completed by the students of the embedded systems Diploma, has been a valuable learning experience. By integrating sensors, controllers, and user interfaces, we successfully designed and built a functional electric water heater prototype.
This project not only reinforced our understanding of embedded systems but also highlighted the practical applications of these technologies in everyday devices. We have gained hands-on experience with hardware and software integration, and our prototype demonstrates effective temperature control and energy management.
Overall, the project has been a rewarding exercise in applying theoretical knowledge to real-world problems, and it has prepared us for future challenges in the field of embedded systems.